RVPC
User Manual
Document v1.3 Nov 2024
www.olimex.com
# What is RVPC?

RVPC is an attempt to produce a very low-cost EURO 1.00 educational computer with RISC-V processor which has everything one complete computer has: keyboard input, VGA display output, and audio output.
The idea of RVPC was born from this TuxCon 2024 talk https://youtu.be/YlYE9a7zsqY.
The goal set was:
1. Easy to solder DIY kit;
2. Complete all in one RISC-V computer with bare minimum Woz like monitor which will allow you to learn the RISC-V instructions by poking, peeking and disassembling the memory
3. Price of EUR 1.00!
Here is the result:
CH32V003 in SO8 package – for easy soldering was chosen. It has just 6 GPIOs:
- PS2 takes two GPIOs
- VGA takes three GPIOs – Vsync, Hsync and RGB
- Audio buzzer is connected to the last GPIO
All done using beginner-friendly PTH components!

## Order codes for RVPC and accessories:

RVPC	Do It Yourself soldering kit
SY0605E	5V power supply adapter
PS2-KEYBOARD	PS2 keyboard
ESP32-S2-DevKitLiPo-USB	ESP32-S2 development board which can be used as CH32V003
programmer
USB-CABLE-A-MICRO-1.8M	USB cable for the programmer
# HARDWARE
## RVPC layout:

PS2 keyboard connector

Buzzer

VGA display

+5V power
jack
Power supply LED indicator
CH32V003 programming

## RVPC schematic:
## RPVC assembly cheat sheet:

## Necessary tools:

Wire Cutters:	we recommend PGC-TR25 these are sharp and light
Tweezers:	we recommend PGC-00SA
Soldering iron:	CHN-SLD802 is budged solution, SLD-FAST-75W is professional solution
Soldering wire:	we recommend Solder-Wire-SAC0307-0-8

## General tips for soldering:
1. Switch on the soldering iron, setup the working temperature to 350 C. Wait until the soldering iron reaches the temperature – there is a LED indicator which will pulse when the temperature is reached;
2. Before soldering, clean the soldering tip with wet sponge from the black residues;
3. Never touch the heated soldering tip or body with bare hands;
4. Be careful to not touch surrounding objects with the soldering iron heated body or tip (cables, table, cloths, etc);
5. Do not leave the soldering iron unattended;
6. Place the electronic component on its place, watch out if there is polarity or orientation;
7. Touch the component pad with the soldering tip which you want to solder and wait 3-4 seconds to heat up;
8. Feed a little from the soldering wire between the soldering tip and the pad until the component lead is flooded with tin and it’s shinny and glossy;
9. If the soldering is not shinny but dull please re-solder with colophon.

# SOFTWARE:

Below is our setup under Linux:
## Install – packages
$ apt-get install build-essential libnewlib-dev gcc-riscv64-unknown-elf libusb-1.0-0-dev libudev-dev gdb-multiarch
## Install – Visual Studio Code
Described here: https://code.visualstudio.com/docs/setup/linux

## Install – Platform IO
Described here: https://platformio.org/install/ide?install=vscode
## Install – CH32V-Platform
https://github.com/Community-PIO-CH32V/ch32-pio-projects?tab=readme-ov-file#installing-the-ch32v-platform
by default the platformio generates only .elf file, to build firmware.bin and firmware.elf select
> PlatformIO > PROJECT TASKS > Default > Advanced > Verbose build

Sample Beeper project is in RVPC repository.
## Prepare the CH32V003 programmer

ESP32-S2-DevKitLiPo-USB can be used as programmer.
The repo with all files required to prepare the ESP32-S2 board as programmer is here – after you have the resources the algorithm to prepare the programmer is:
1. Press and hold the Boot button and connect the USB cable, the yellow LED will stay ON
check with
$ls /dev/ttyA*
which is the ttyACM it’s usually 0 or 1
execute this command:
$ python3 ./rvpc/esptool/esptool.py -p /dev/ttyACM0 -b 460800 --before=no_reset --after=no_reset write_flash --flash_mode dio --flash_freq 80m --flash_size 4MB 0x1000 ./rvpc/esp32s2/bootloader.bin 0x10000 ./rvpc/esp32s2/usb_sandbox.bin 0x8000 ./rvpc/esp32s2/partition-table.bin
check if the programmer is already OK with
$ dmesg
you have to see this message:
hid-generic 0003:303A:4004.0015: input,hidraw5: USB HID v1.11 Gamepad [CNLohr ESP32-S2 CH32V003Programmer] on usb-0000:00:14.0-2/input0
which means the ESP32-S2-DevKitLipo-USB now acts as a programmer and can be used with the demo project above from PlatformIO, but first you have to enable it with:
$ sudo cp ./rvpc/tools/ch32v003fun/minichlink/99-minichlink.rules /etc/udev/rules.d/
$ sudo udevadm control --reload-rules && sudo udevadm trigger

Now you can use GPIO6 and GND to connect to RVPC programming connector PGM-GND

Now CH32V003 flashing will work directly from PlatformIO but if you want to use command line this is the command:
./rvpc/tools/ch32v003fun/minichlink/minichlink -w ./firmware.bin 0x08000000

## Create project:

If you create a new project to enable the ESP32-S2 programmer you should edit platformio.ini and add this line
upload_protocol = minichlink

It’s already added to the demo project.
## RVPC monitor demo RVMON (default)

The chip of RVPC comes programmed with this RVPC monitor demo. All demos can be found here:

https://github.com/OLIMEX/RVPC/tree/main/SOFTWARE

This is WOZ-like monitor which allow you to display memory, write to memory and execute code.
The list of all commands are displayed with “?”
## Towers of Hanoi demo

This is original game created by Curtis Whitley who wrote the VGA display code for RVPC.

## Towers of Hanoi Interactive demo

This is modified version which uses the keyboard so user can tell which disk to which tower go.
## TETRIS demo

This is the very popular game made for RVPC.
# Revision History
Revision 1.0 June 2024
Revision 1.1 September 2024
Revision 1.2 October 2024 add assembly instructions
Revision 1.3 November 2024 improved instructions