RVPC
User Manual
Rev.1.2	October 2024	olimex.com
# What is RVPC?

RVPC is an attempt to produce very low cost EURO 1.00 educational computer with RISC-V processor which to have everything one complete computer have: Keyboard input, VGA display output and Audio output.
The idea of RVPC evolved on TuxCon 2024 as a Lighting talk https://youtu.be/YlYE9a7zsqY.
The goal set was:
1. Easy to solder DIY kit
2. Complete all in one RISC-V computer with bare minimum Woz like monitor which will allow you to learn the RISC-V instructions by poking, peeking and disassembling the memory
3. Price of EUR 1.00!
Here is the result:
CH32V003 in SO8 package – for easy soldering was chosen. It has just 6 GPIOs
- PS2 takes two GPIOs
- VGA takes three GPIOs – Vsync, Hsync and RGB
- Audio buzzer is connected to the last GPIO
All done in beginner friendly PTH components

## Order codes for RVPC and accessories:

RVPC	Do It Yourself soldering kit
SY0605E	5V power supply adapter
PS2-KEYBOARD	PS2 keyboard
ESP32-S2-DevKitLiPo-USB	ESP32-S2 development board which can be used as CH32V003
programmer
USB-CABLE-A-MICRO-1.8M	USB cable for the programmer
# HARDWARE

## RVPC layout:

PS2 keyboard connector

Buzzer
VGA display

+5V power
jack

Power supply LED indicator

CH32V003 programming

## RVPC schematic:
# RPVC assembly:

# Necessary tools:
# Wire Cutters: we recommend PGC-TR25 they are sharp and light
# Twizzers: we recommend PGC-00SA
# Soldering iron: CHN-SLD802 is budged solution, SLD-FAST-75W is professional solution
# Soldering wire: we recommend Solder-Wire-SAC0307-0-8
# General tips for soldering:
# 1. Switch On the soldering iron, setup the working temperature to 350 C. Wait until the Soldering
# Iron reach this temperature – there is LED indicator which will pulse when the temperature is reach.
# 2. Before soldering clean the Soldering tip with wet sponge from the black resedues.
# 3. Never touch the heated soldering tip or body.
# 4. Do not leave the Soldering Iron unattended.
# 5. Be careful to not touch cables, table, cloths with the soldering iron heated body or tip.
# 6. Place the electronic component on it’s place, watch out if there is polarity.
# 7. Touch the component pad which you want to solder and wait 3-4 seconds to heat up.
# 8. Feed a little from the soldering wire until the component lead is flooded with tin and it’s shinny
# and glossy.
# 9. If the soldering is not shinny but dull please re-solder with colophony.
# SOFTWARE:

Here below is our setup under Linux:
### Install - packages
$ apt-get install build-essential libnewlib-dev gcc-riscv64-unknown-elf libusb-1.0-0-dev libudev-dev gdb-multiarch
### Install - Visual Studio Code
Described here: https://code.visualstudio.com/docs/setup/linux

### Install - Platform IO
Described here: https://platformio.org/install/ide?install=vscode
### Install - CH32V-Platform
https://github.com/Community-PIO-CH32V/ch32-pio-projects?tab=readme-ov-file#installing-the-ch32v-platform
by default the platformio generates only .elf file, to build firmware.bin and firmware.elf select
> PlatformIO > PROJECT TASKS > Default > Advanced > Verbose build

Sample Beeper project is in RVPC repository.
### Prepare the CH32V003 programmer

ESP32-S2-DevKitLiPo-USB can be used as programmer.
The firmware is here you can build from sources or you can download the ready built binaries from here and use this sequence to prepare the programmer:
1. hold the Boot button and connect the USB cable, the yellow LED will stay ON
check with
$ls /dev/ttyA*
which is the ttyACM it’s usually 0 or 1
execute this command:
$ python3 ./rvpc/esptool/esptool.py -p /dev/ttyACM0 -b 460800 --before=no_reset --after=no_reset write_flash --flash_mode dio --flash_freq 80m --flash_size 4MB 0x1000 ./rvpc/esp32s2/bootloader.bin 0x10000 ./rvpc/esp32s2/usb_sandbox.bin 0x8000 ./rvpc/esp32s2/partition-table.bin

check if the programmer is already OK with
$ dmesg
you have to see this message:
hid-generic 0003:303A:4004.0015: input,hidraw5: USB HID v1.11 Gamepad [CNLohr ESP32-S2 CH32V003Programmer] on usb-0000:00:14.0-2/input0
which means the ESP32-S2-DevKitLipo-USB now act as programmer and can be used with the demo project above from PlatformIO, but first you have to enable it with:
$ sudo cp ./rvpc/tools/ch32v003fun/minichlink/99-minichlink.rules /etc/udev/rules.d/
$ sudo udevadm control --reload-rules && sudo udevadm trigger

Now you can use GPIO6 and GND to connect to RVPC programming connector PGM-GND

Now CH32V003 flashing will work directly from PlatformIO but if you want to use command line this is the command:
./rvpc/tools/ch32v003fun/minichlink/minichlink -w ./firmware.bin 0x08000000

### Create project:

If you create new project to enable the ESP32-S2 programmer you should edit platformio.ini and add this line
upload_protocol = minichlink

It’s already added to the demo project.
### RVPC monitor
# This is WOZ like monitor which allow you to display memory, write to memory and execute code.
# The list of all commands are displayed with “?”
### Towers of Hanoi

This is original game created by Curtis Whitley who wrote the VGA display code for RVPC.

### Towers of Hanoi Interractive

This is modified version which uses the keyboard so user can tell which disk to which tower go.
### TETRIS

This is the very popular game made for RVPC.
# Revision History
Revision 1.0 June 2024
Revision 1.1 September 2024
Revision 1.2 September 2024 add assembly instructions